## Slide 1
TODAY
Week 04–05 update: evidence changed the direction
Week 04–05 group meeting | Robotic systems in battery manufacturing
01
Main message: One candidate became a baseline; I returned to clearer robotics cases.
1. What I did
Audited cell-finishing carrier flow
Tested one formation-loading interface
2. What is the problem
Battery-specific conditions did not clearly change the fixed transfer task.
3. What I need
Thomas decision on scope, case priority, humanoid role, and validation access.
Notes: Today I will give a concise Week 03 update around the same three questions: what I did, what problem I found, and what I will do next week. In response to the last feedback, I stopped comparing several robotics candidates at a high level and selected one learning case: tray transport between formation, aging, and end-of-line testing. I then decomposed this case from the process functions to transport requests, waiting, and equipment handover. The main progress is therefore not a final AGV model. It is a more concrete, process-specific understanding of what the transport system would actually need to do.

## Slide 2
WEEK 04
Existing research already covers configurations and interfaces.
Sources: Wanner et al. 2022; Schomburg et al. 2024; Deng et al. 2026; Lee et al. 2024 | Evidence boundaries retained
02
Evidence
What I established
Research implication
State of the art
Manual and fully automated tray-based configurations exist.
‘Fully automated’ does not prove AGV transport.
Carrier role
Some carriers also provide contact, fixture, or controlled pressure.
A carrier is not always a passive logistics unit.
Counterexample
Deng models physical interfaces and intralogistics transitions.
No claim that interfaces or logistics were never studied.
Week 04 decision
Kept handover and exception flow only as testable candidates.
No final gap; no simulation without a validated task.
Notes: I decomposed the selected case into four layers. First, I separated the functions of formation, room-temperature aging, end-of-line testing, and grading, because they do not create the same process or storage requirements. Second, I examined the carrier flow and learned that two neighboring process steps do not automatically create a transport task; a task exists only when the locations are separated and the carrier must move. Third, I separated process completion, load release, request creation, waiting, pickup, delivery, destination acceptance, and the final state update. Finally, I distinguished fleet sizing, dispatching, routing, traffic control, and physical handover instead of calling everything AGV scheduling. This gives me a clearer basis for later modelling and validation.

## Slide 3
WEEK 05
One formation-loading architecture became a bounded baseline.
Source: CN118970237A, description [0061]–[0062] | Patent disclosure, not deployment validation
03
Layer
Direct evidence
Evidence boundary
Architecture
Inbound machine 27 → stacker crane 28 → formation equipment 3.
Fixed automation; not an AGV deployment.
Flow object
A carrier/tray holds multiple cells and is transferred into formation.
Pickup port, receiving port, and final contact remain unknown.
Responsibility audit
Tested position, locking, contact, identity, and readiness.
No same-case evidence that they change the stacker-crane task.
Week 05 decision
Retain B2 as a fixed-automation baseline and counterexample.
Exit the thesis-candidate path; return to the robotics map.
Notes: I decomposed the selected case into four layers. First, I separated the functions of formation, room-temperature aging, end-of-line testing, and grading, because they do not create the same process or storage requirements. Second, I examined the carrier flow and learned that two neighboring process steps do not automatically create a transport task; a task exists only when the locations are separated and the carrier must move. Third, I separated process completion, load release, request creation, waiting, pickup, delivery, destination acceptance, and the final state update. Finally, I distinguished fleet sizing, dispatching, routing, traffic control, and physical handover instead of calling everything AGV scheduling. This gives me a clearer basis for later modelling and validation.

## Slide 4
THE PROBLEM
The missing link is a battery requirement that changes a robot task.
Direction criterion: Thomas original thesis brief + Week 05 robotics-relevance gate
04
Direct battery evidence
YES
The architecture belongs to cell formation and moves a battery carrier.
Battery effect on robot task
NO DIRECT EVIDENCE
Identity is known; locking, contact, and precision are not shown to alter the transfer task.
Validation route
NOT ESTABLISHED
No accessible interface, expert, or dataset confirms a meaningful remaining problem.
Notes: The main problem is now more specific than simply saying that data are missing. The literature supports several parts of the model: cell-finishing routes vary by manufacturer and cell format, AGV systems contain different design and control decisions, and there is at least one real AGV case in rechargeable-battery production. However, the connection to our selected tray-flow case is still conditional. I can infer that physical separation and carrier relocation create a transport task, and that delays may cause blocking or starvation under certain buffer conditions. But the cell format, transport unit, tray continuity, handover interface, layout, takt time, empty-carrier flow, AGV number, and even the use of AGVs are still unknown. Therefore, this is a conceptual model, not a confirmed factory scenario.

## Slide 5
DIRECTION RESET
Three candidates restore an explicit robot actor and task.
Evidence: direct company disclosures define tasks; performance and maturity remain independently unverified
05
B — Pack EoL/DCR connectors
Locate, insert, verify, and remove flexible test connectors.
Compare dedicated automation, fixed robots, and mobile/humanoid systems.
CONDITIONAL PRIMARY
A — Cell grasping & loading
Identify incoming cells, plan the grasp, pick, and load for module/pack assembly.
Needs a clearer destination and interface.
STRONG BACKUP
C — Multi-station handling
Module/pack material handling and picking across stations.
Flow object, handover, and battery-specific effect remain unclear.
EXPLORATORY
All three remain candidates; each needs a battery-specific requirement, baseline, and validation route.
Notes: To test the evidence boundary, I studied the closest public AGV case I found in rechargeable-battery production. The case is valuable because it uses actual job records and a real site configuration with nine AGVs, one hundred ports, and four charging stations, and it evaluates an idle-vehicle parking policy. However, the paper does not disclose what material is transported or which battery process is involved. It does not mention formation, aging, end-of-line testing, trays, or the handover interface. I therefore use it as direct evidence that an AGV-system problem exists in battery production, but only as adjacent evidence for my cell-finishing case. I should not transfer its reported performance results or parameters to my scenario without process-specific evidence.

## Slide 6
THOMAS DECISION
Next week should lock one case—not expand the map again.
Decision gate derived from the original thesis brief and the Week 04–05 evidence audit
06
1. Confirm scope
Can module/pack manufacturing become the primary case?
Which product format and production environment should anchor it?
2. Choose case + robot role
Prioritize B, A, or C.
Is humanoid the main technology, one comparison architecture, or a future trend?
3. Confirm validation
Which PEM/FFB/industry station, expert, equipment specification, or dataset is realistically accessible?
Next week: lock one case charter—task, battery requirement, baseline, method, evidence, and validation.
Notes: Next week I will test whether the possible research gap is real before I define a simulation study. First, I will search specifically for research that connects cell finishing, carrier flow, and AGV or material-handling design, and I will classify the results as direct, adjacent, or false matches. Second, I will build one comparison table and actively search for counterexamples that may already connect process constraints with mobile transport decisions. Third, I will keep only one or two candidate gaps and convert the remaining unknown interfaces and parameters into focused expert questions. At this point, I would like to ask whether this level of decomposition is concrete enough, and whether I should prioritize academic counterexamples or industrial interface evidence in the next step.