## Slide 1
TODAY
Week 04–05 update: evidence changed the direction
Week 04–05 group meeting | Robotic systems in battery manufacturing
01
Main message: One candidate became a baseline; I returned to clearer robotics cases.
1. What I did
Audited cell-finishing carrier flow
Tested one formation-loading interface
2. What is the problem
Battery-specific conditions did not clearly change the fixed transfer task.
3. What I need
Thomas decision on scope, case priority, humanoid role, and validation access.
Notes: Good morning. Today I will briefly report the progress from Week 4 and Week 5.
In Week 4, I reviewed the state of the art for carrier flow in cell finishing and actively searched for counterexamples. In Week 5, I tested one concrete formation-loading architecture.
The important result is not a final research gap. Instead, the evidence showed that the old formation-handover candidate should be retained only as a fixed-automation baseline. I therefore returned to the original thesis objective and prepared three clearer robotics cases.
At the end, I need Thomas's feedback on the scope, the case priority, the role of humanoid robots, and a realistic validation route.
Transition: First, I will summarize what the Week 4 literature audit actually established.

## Slide 2
WEEK 04
Existing research already covers configurations and interfaces.
Sources: Wanner et al. 2022; Schomburg et al. 2024; Deng et al. 2026; Lee et al. 2024 | Evidence boundaries retained
02
Evidence
What I established
Research implication
State of the art
Manual and fully automated tray-based configurations exist.
‘Fully automated’ does not prove AGV transport.
Carrier role
Some carriers also provide contact, fixture, or controlled pressure.
A carrier is not always a passive logistics unit.
Counterexample
Deng models physical interfaces and intralogistics transitions.
No claim that interfaces or logistics were never studied.
Week 04 decision
Kept handover and exception flow only as testable candidates.
No final gap; no simulation without a validated task.
Notes: In Week 4, I followed the sequence suggested by Thomas: first describe the state of the art, then identify problem areas, and only afterward discuss a possible gap.
The literature shows both manual and fully automated tray-based configurations in cell finishing. However, fully automated does not automatically mean AGV transport.
I also learned that a formation carrier may do more than transport. In some configurations, it supports contact, fixture, or controlled-pressure functions.
The strongest counterexample was the work by Deng and colleagues. It already models physical interfaces and some intralogistics transitions. Therefore, I cannot claim that cell-finishing logistics or interfaces have never been studied.
My Week 4 decision was to keep handover and exception flow only as testable candidates. I did not define a final gap and did not start simulation.
Transition: In Week 5, I tested the handover candidate using one concrete public architecture.

## Slide 3
WEEK 05
One formation-loading architecture became a bounded baseline.
Source: CN118970237A, description [0061]–[0062] | Patent disclosure, not deployment validation
03
Layer
Direct evidence
Evidence boundary
Architecture
Inbound machine 27 → stacker crane 28 → formation equipment 3.
Fixed automation; not an AGV deployment.
Flow object
A carrier/tray holds multiple cells and is transferred into formation.
Pickup port, receiving port, and final contact remain unknown.
Responsibility audit
Tested position, locking, contact, identity, and readiness.
No same-case evidence that they change the stacker-crane task.
Week 05 decision
Retain B2 as a fixed-automation baseline and counterexample.
Exit the thesis-candidate path; return to the robotics map.
Notes: In Week 5, I examined the public patent CN118970237A as a bounded reference architecture.
The source explicitly describes a carrier moving from inbound machine 27, through stacker crane 28, into formation equipment 3. This helped me distinguish regional transport, fixed final loading, and the internal process equipment.
The architecture is fixed automation. It is not evidence of an AGV deployment. The exact pickup port, receiving port, final contact, and equipment-acceptance logic are also not fully disclosed.
I then audited possible requirements such as positioning, locking, contact, identity, and readiness. In this same case, I found no direct evidence that these conditions change the task of the stacker crane.
Therefore, I retained B2 as a useful fixed-automation baseline and counterexample, but removed it from the thesis-candidate path.
Transition: The next slide explains exactly why this candidate did not pass the robotics-relevance gate.

## Slide 4
THE PROBLEM
The missing link is a battery requirement that changes a robot task.
Direction criterion: Thomas original thesis brief + Week 05 robotics-relevance gate
04
Direct battery evidence
YES
The architecture belongs to cell formation and moves a battery carrier.
Battery effect on robot task
NO DIRECT EVIDENCE
Identity is known; locking, contact, and precision are not shown to alter the transfer task.
Validation route
NOT ESTABLISHED
No accessible interface, expert, or dataset confirms a meaningful remaining problem.
Notes: The old candidate failed because one important link was missing: a battery-specific requirement that clearly changes a robot task or a robot–equipment integration decision.
The first gate is direct battery-manufacturing evidence. This gate is passed, because the architecture belongs to cell formation and moves a battery carrier.
The second gate is the battery-specific effect on the robot task. Here, the evidence is insufficient. Carrier identity is mentioned, but locking, contact, and precision are not shown to change the transfer task of the stacker crane.
The third gate is validation. I currently have no accessible interface, expert, equipment data, or dataset that confirms an important remaining problem.
This means that missing public detail is not automatically a research gap. Continuing into PLC states or formation-equipment contact would move the thesis away from the original robotics-application objective.
Transition: I therefore returned to the original thesis brief and compared three clearer robot-application cases.

## Slide 5
DIRECTION RESET
Three candidates restore an explicit robot actor and task.
Evidence: direct company disclosures define tasks; performance and maturity remain independently unverified
05
B — Pack EoL/DCR connectors
Locate, insert, verify, and remove flexible test connectors.
Compare dedicated automation, fixed robots, and mobile/humanoid systems.
CONDITIONAL PRIMARY
A — Cell grasping & loading
Identify incoming cells, plan the grasp, pick, and load for module/pack assembly.
Needs a clearer destination and interface.
STRONG BACKUP
C — Multi-station handling
Module/pack material handling and picking across stations.
Flow object, handover, and battery-specific effect remain unclear.
EXPLORATORY
All three remain candidates; each needs a battery-specific requirement, baseline, and validation route.
Notes: The original thesis brief asks me to start from manufacturing requirements, identify suitable robot applications, assess them technically and economically, and develop concrete implementation scenarios.
Candidate B is flexible test-connector handling in Pack EoL or DCR testing. The task is to locate, insert, verify, and remove flexible test connectors. It provides a useful comparison between dedicated automation, fixed industrial robots, and mobile or humanoid systems. This is my conditional primary candidate.
Candidate A is cell recognition, grasping, and loading for module or pack assembly. It has relatively clear company evidence and is my strong backup, but the exact destination and loading interface still need clarification.
Candidate C is multi-station module or pack handling and picking. It is exploratory because the flow object, handover, and battery-specific effect are still unclear.
All three remain candidates. Company disclosures support the reported tasks, but they do not independently validate performance, maturity, or economic advantage.
Transition: Before I deepen any of them, I need three decisions from Thomas.

## Slide 6
THOMAS DECISION
Next week should lock one case—not expand the map again.
Decision gate derived from the original thesis brief and the Week 04–05 evidence audit
06
1. Confirm scope
Can module/pack manufacturing become the primary case?
Which product format and production environment should anchor it?
2. Choose case + robot role
Prioritize B, A, or C.
Is humanoid the main technology, one comparison architecture, or a future trend?
3. Confirm validation
Which PEM/FFB/industry station, expert, equipment specification, or dataset is realistically accessible?
Next week: lock one case charter—task, battery requirement, baseline, method, evidence, and validation.
Notes: For next week, I do not want to expand the application map again. I want to lock one case and build one case charter.
First, I need confirmation of the scope. Can module and pack manufacturing become the primary case within this thesis, although the task paragraph refers to the battery-cell production value chain? We should also select one product format and production environment.
Second, I need a case and technology decision. Should I prioritize B, A, or C? Should humanoid robots be the main technology, one architecture within a comparison, or mainly a future-trend scenario?
Third, I need a realistic validation route. Is there a PEM, FFB, or industry station, an equipment or integration expert, a specification, or a dataset that I can actually access?
If these points are confirmed, the minimum output next week will be one case charter: the task, battery requirement, comparison baseline, method, evidence minimum, and validation route.
Closing question: Which candidate and validation path should I deepen first?