## Slide 1
WEEK 06 UPDATE
Week 06 turned one use case into a repeatable assessment method.
Sources: Week 06 Day 1–5 synthesis; 2026-08-26 Thomas meeting outline; registration consensus 2026-08-20.
01
Pack EoL test-connector handling was the deep reference case—not the final thesis boundary.
1 What I did
• Decomposed the connector-handling cycle and system responsibilities
• Derived six task and production requirements
• Built Framework v0.1 for architecture assessment
2 What is the problem
• The task is flexible, contact-rich and safety-gated
• Evidence strength is unequal across architectures
• Current evidence cannot support a global ranking
3 Next week
• Run one bounded transfer test on cell identification, grasping and loading
• Confirm title, RQs and production-level scope with Thomas
FRAMEWORK v0.1
Task → Requirements → Capabilities → Conditional suitability → Evidence-bounded decision
The method is reusable; the Pack-specific answers are not.
Notes: Good morning. Today I will report the main outcome of Week 6 and the proposed next step.
I used battery-pack end-of-line test-connector handling as a deep reference case. The goal was not to evaluate one company or prove that a humanoid robot is superior. I decomposed the task and system responsibilities, derived six relevant requirements, and built the first version of a task-based assessment framework.
The central logic is: task, requirements, capabilities, conditional suitability and an evidence-bounded decision. The Pack EoL case develops the method; it is not the final thesis boundary.
The remaining problem is unequal evidence strength across architectures, so current evidence does not support a global ranking. Next, I propose a bounded transfer test on cell identification, grasping and loading, while confirming the title, research questions and production-level scope with Thomas.
Transition: First, I will clarify what the robot actually does in the Pack EoL task.

## Slide 2
WHAT I DID
The robot connects the tester; it does not perform the electrical test.
Reference abstraction from Pack EoL equipment baselines, company disclosure and engineering reasoning; not a CATL site reconstruction.
02
STATION / MES
Pack positioned
and identified
PLC / SAFETY
Safe-to-connect
permission
ROBOT
Locate & support → align →
insert → confirm
TESTER
Electrical and
functional EoL test
PLC + ROBOT
De-energize → remove
→ return harness
→
→
→
→
REFERENCE RESPONSIBILITY BOUNDARY
Robot / connector automation
physical connector and harness manipulation
Test equipment
electrical measurement and test execution
PLC / safety
permissions, interlocks, safe state and safe stop
MES / traceability
pack identity, recipe and result association
EVIDENCE BOUNDARY
This is a reference abstraction.
The actual CATL task allocation, safety sequence and connector geometry remain UNKNOWN.
Notes: This slide separates the physical robot task from the electrical test process.
The pack is first positioned and identified. The PLC and safety system then provide permission to connect. Only after this permission does the robot locate and support the harness, align and insert the connector, and confirm the physical connection.
The test equipment—not the robot—performs the electrical and functional EoL test. Afterwards, the tester and PLC confirm that the system is de-energized and safe to disconnect. The robot removes the connector and returns the harness, while MES links the recipe and result to the pack identity.
This responsibility boundary prevents the robot task, test process and safety logic from being mixed together, and it identifies the interfaces required for implementation.
This is a reference abstraction, not a reconstruction of the CATL station. The actual task allocation, connector geometry and safety sequence remain unknown.
Transition: Based on this task cycle, I derived the requirements that actually change the robotic task.

## Slide 3
WHAT IS THE PROBLEM
Six requirements turn a simple plug-in action into a robotics-system problem.
Source: Week 06 Day 3 requirement audit. R3 is the only fully battery-specific requirement; R1/R2/R5/R6 are hybrid constraints.
03
PHYSICAL MANIPULATION
R1 Flexible-harness handling
R2 Contact-rich insertion
Changing pose, tension and contact forces demand perception, support, compliance and recovery.
PROCESS & SAFETY
R3 Electrical / HV safety interface
R5 Connection-quality confirmation
The robot acts only under safe-state permission; insertion must be confirmed, not merely completed geometrically.
BATTERY-SPECIFIC
PRODUCTION & INTEGRATION
R4 Variation and changeover
R6 Traceability and integration
Programs, tooling and records must remain linked to pack identity, recipe and exception handling.
CRITICAL UNKNOWNS
connector geometry & force
safe-state handshake
actual confirmation logic
cycle, reliability & cost
Notes: The connector task is more than a simple pick-and-place or a geometric plug-in action. I grouped the six requirements into three layers.
The first layer is physical manipulation. R1 is flexible-harness handling: connector pose changes with gravity, grasp point and cable history. R2 is contact-rich insertion: after contact, geometry alone is insufficient, so the system needs compliance, force sensing and recovery.
The second layer is process and safety. R3 is the electrical and high-voltage safety interface. The robot must follow safe-state permissions and interlocks. R5 is connection-quality confirmation, because physical insertion does not prove correct locking or electrical connection.
The third layer is production and integration. R4 covers variation and changeover; R6 covers traceability and synchronization with the PLC, tester and MES.
R3 is the strongest fully battery-specific gate. The other requirements also occur elsewhere, but the battery context changes their consequences and validation needs.
Key unknowns remain: connector geometry and force, the safety handshake, confirmation logic, and independent cycle, reliability and cost data.
Transition: These requirements do not produce one universal winner; the answer changes with the production scenario.

## Slide 4
WEEK 06 FINDING
Production conditions and evidence strength change architecture suitability.
Sources: Week 06 Day 4–5 architecture audit. Scenarios are illustrative, not descriptions of the CATL line.
04
LOW VARIETY · HIGH VOLUME
Prioritise dedicated automation
Fixtures and mechanical guidance can absorb part of the handling complexity at one stable interface.
SUPPORTED BY EQUIPMENT BASELINES
MODERATE VARIATION · FIXED STATION
Prioritise a fixed industrial robot
Vision, force control and programmable motion address R1/R2/R5; changeover remains manageable.
STRONGEST ROBOTICS BASELINE
HIGH VARIATION · MULTI-STATION · BROWNFIELD
Evaluate mobile dual-arm / humanoid
Mobility and two-arm support may create value across stations, but R3 safety, maturity and economics remain unresolved.
CONDITIONAL / KEY UNKNOWNS
A technology passes deployment only when all four checks are credible:
TASK GATE
Can it satisfy the critical requirement?
CONDITION GATE
Is this architecture reasonable here?
SAFETY GATE
Can mandatory permissions be satisfied?
EVIDENCE GATE
Is the claim supported strongly enough?
Notes: The main Week 6 finding is conditional suitability, not architecture ranking.
For low variety, high volume, a fixed interface and one station, dedicated automation should be prioritized. Fixtures and mechanical guidance can absorb part of the handling complexity, and equipment baselines support this conclusion.
With moderate variation and a stationary task, a fixed industrial robot is the strongest robotics baseline. Vision, force control and programmable motion address harness handling, insertion and confirmation. Its boundary appears when several stations require robot replication or layout modification.
Under high variation, multiple stations and a human-oriented brownfield layout, a mobile dual-arm or humanoid system is worth evaluating. However, current evidence does not establish battery-specific safety integration, long-term reliability, maturity or economic superiority.
Each architecture must therefore pass four checks: can it satisfy the task, is it reasonable under these production conditions, can mandatory safety permissions be fulfilled, and is the evidence strong enough for the intended claim?
Transition: The next week should test whether this reasoning can be transferred beyond the Pack EoL case.

## Slide 5
NEXT WEEK PLAN
Next week should test transferability and confirm the registration basis.
Sources: Week 06 Day 5 transfer decision; thesis registration consensus 2026-08-20. Title/RQs remain pending Thomas confirmation.
05
BOUNDED TRANSFER TEST — CANDIDATE A
01
Define the task boundary
Source → destination → completion criterion → battery-specific effect
→
02
Run the same questions
Task → requirements → baseline → capabilities → conditional suitability
→
03
Compare what transfers
Keep the assessment logic; re-derive the case-specific answers and evidence needs
THOMAS — THREE DECISIONS
1
Registration proposal
Confirm or revise the proposed title and three RQs.
2
Production-level scope
Explicitly include selected module/pack cases alongside cell-production applications?
3
Research route
Deep case → framework → adjacent case(s) → cross-case comparison?
WEEK 06 STATUS
DEEP CASE CONTINUES
NARROW CLAIM
FRAMEWORK TRANSFER READY
PROPOSED TITLE — PENDING
Task-Based Assessment of Robotic Systems in Battery Manufacturing
Notes: My proposed next step is one bounded transfer test on Candidate A: cell identification, grasping and loading in module or pack manufacturing.
First, I will define the source, destination, completion criterion and battery-specific effect before comparing robots. Week 5 showed that merely moving an object from A to B does not establish a robotics problem.
Second, I will apply the same questions: task, requirements, baseline, capabilities and conditional suitability. Third, I will compare what transfers. The assessment logic should transfer, but Pack-specific answers such as harness handling and connector insertion must be re-derived rather than copied.
I also need three decisions from Thomas: whether the proposed title and three research questions should be accepted or revised; whether selected module- and pack-level applications should be explicitly included alongside cell-production applications; and whether the route from one deep case, through a transferable framework and adjacent cases, to a cross-case comparison matches the intended thesis profile.
The Week 6 status is: the deep case continues, the claims remain narrow and evidence-bounded, and the framework is ready for a first transfer test.
Closing: The outcome is not that one robot is best. It is a first repeatable procedure connecting a battery-manufacturing task to requirements, capabilities, production conditions and defensible implementation decisions.