## Slide 1
WEEK 06 UPDATE
Week 06 turned one use case into a repeatable assessment method.
Sources: Week 06 Day 1–5 synthesis; 2026-08-26 Thomas meeting outline; registration consensus 2026-08-20.
01
Pack EoL test-connector handling was the deep reference case—not the final thesis boundary.
1 What I did
• Decomposed the connector-handling cycle and system responsibilities
• Derived six task and production requirements
• Built Framework v0.1 for architecture assessment
2 What is the problem
• The task is flexible, contact-rich and safety-gated
• Evidence strength is unequal across architectures
• Current evidence cannot support a global ranking
3 Next week
• Run one bounded transfer test on cell identification, grasping and loading
• Confirm title, RQs and production-level scope with Thomas
FRAMEWORK v0.1
Task → Requirements → Capabilities → Conditional suitability → Evidence-bounded decision
The method is reusable; the Pack-specific answers are not.

## Slide 2
WHAT I DID
The robot connects the tester; it does not perform the electrical test.
Reference abstraction from Pack EoL equipment baselines, company disclosure and engineering reasoning; not a CATL site reconstruction.
02
STATION / MES
Pack positioned
and identified
PLC / SAFETY
Safe-to-connect
permission
ROBOT
Locate & support → align →
insert → confirm
TESTER
Electrical and
functional EoL test
PLC + ROBOT
De-energize → remove
→ return harness
→
→
→
→
REFERENCE RESPONSIBILITY BOUNDARY
Robot / connector automation
physical connector and harness manipulation
Test equipment
electrical measurement and test execution
PLC / safety
permissions, interlocks, safe state and safe stop
MES / traceability
pack identity, recipe and result association
EVIDENCE BOUNDARY
This is a reference abstraction.
The actual CATL task allocation, safety sequence and connector geometry remain UNKNOWN.

## Slide 3
WHAT IS THE PROBLEM
Six requirements turn a simple plug-in action into a robotics-system problem.
Source: Week 06 Day 3 requirement audit. R3 is the only fully battery-specific requirement; R1/R2/R5/R6 are hybrid constraints.
03
PHYSICAL MANIPULATION
R1 Flexible-harness handling
R2 Contact-rich insertion
Changing pose, tension and contact forces demand perception, support, compliance and recovery.
PROCESS & SAFETY
R3 Electrical / HV safety interface
R5 Connection-quality confirmation
The robot acts only under safe-state permission; insertion must be confirmed, not merely completed geometrically.
BATTERY-SPECIFIC
PRODUCTION & INTEGRATION
R4 Variation and changeover
R6 Traceability and integration
Programs, tooling and records must remain linked to pack identity, recipe and exception handling.
CRITICAL UNKNOWNS
connector geometry & force
safe-state handshake
actual confirmation logic
cycle, reliability & cost

## Slide 4
WEEK 06 FINDING
Production conditions and evidence strength change architecture suitability.
Sources: Week 06 Day 4–5 architecture audit. Scenarios are illustrative, not descriptions of the CATL line.
04
LOW VARIETY · HIGH VOLUME
Prioritise dedicated automation
Fixtures and mechanical guidance can absorb part of the handling complexity at one stable interface.
SUPPORTED BY EQUIPMENT BASELINES
MODERATE VARIATION · FIXED STATION
Prioritise a fixed industrial robot
Vision, force control and programmable motion address R1/R2/R5; changeover remains manageable.
STRONGEST ROBOTICS BASELINE
HIGH VARIATION · MULTI-STATION · BROWNFIELD
Evaluate mobile dual-arm / humanoid
Mobility and two-arm support may create value across stations, but R3 safety, maturity and economics remain unresolved.
CONDITIONAL / KEY UNKNOWNS
A technology passes deployment only when all four checks are credible:
TASK GATE
Can it satisfy the critical requirement?
CONDITION GATE
Is this architecture reasonable here?
SAFETY GATE
Can mandatory permissions be satisfied?
EVIDENCE GATE
Is the claim supported strongly enough?

## Slide 5
NEXT WEEK PLAN
Next week should test transferability and confirm the registration basis.
Sources: Week 06 Day 5 transfer decision; thesis registration consensus 2026-08-20. Title/RQs remain pending Thomas confirmation.
05
BOUNDED TRANSFER TEST — CANDIDATE A
01
Define the task boundary
Source → destination → completion criterion → battery-specific effect
→
02
Run the same questions
Task → requirements → baseline → capabilities → conditional suitability
→
03
Compare what transfers
Keep the assessment logic; re-derive the case-specific answers and evidence needs
THOMAS — THREE DECISIONS
1
Registration proposal
Confirm or revise the proposed title and three RQs.
2
Production-level scope
Explicitly include selected module/pack cases alongside cell-production applications?
3
Research route
Deep case → framework → adjacent case(s) → cross-case comparison?
WEEK 06 STATUS
DEEP CASE CONTINUES
NARROW CLAIM
FRAMEWORK TRANSFER READY
PROPOSED TITLE — PENDING
Task-Based Assessment of Robotic Systems in Battery Manufacturing