## Slide 1
TODAY
Week 03 update: one case, decomposed step by step
Week 03 group meeting | Robotic systems in battery manufacturing
01
Main message: I moved from a high-level map to a process-specific model of cell-finishing tray transport.
1. What I did
Selected formation–aging–EoL tray flow
Mapped process, requests, waiting, and handover
2. What is the problem
The task model is conditional; layout, carrier flow, interfaces, and AGV use remain unconfirmed.
3. Next week
Search nearest-neighbor research and counterexamples before defining a gap or simulation.
Notes: Today I will give a concise Week 03 update around the same three questions: what I did, what problem I found, and what I will do next week. In response to the last feedback, I stopped comparing several robotics candidates at a high level and selected one learning case: tray transport between formation, aging, and end-of-line testing. I then decomposed this case from the process functions to transport requests, waiting, and equipment handover. The main progress is therefore not a final AGV model. It is a more concrete, process-specific understanding of what the transport system would actually need to do.

## Slide 2
WHAT I DID
I decomposed one case from process functions to AGV execution.
Sources: Kampker et al. 2023, pp. 2–10; Plumeyer et al. 2023, pp. 3–6; VDA 5050 v3.0.0, pp. 6–38
02
Layer
What I established
Why it matters
Process logic
Formation, RT aging, EoL, and grading serve different functions.
Route and storage logic generate logistics needs.
Carrier flow
Transport exists only if locations differ and the carrier must move.
Avoids assuming one tray or one standard route.
Transport task
Release → request → wait → pickup → delivery → acceptance + state update.
Vehicle arrival alone does not complete the task.
System logic
Separated fleet sizing, dispatching, routing, traffic control, and handover.
Turns ‘AGV scheduling’ into testable questions.
Notes: I decomposed the selected case into four layers. First, I separated the functions of formation, room-temperature aging, end-of-line testing, and grading, because they do not create the same process or storage requirements. Second, I examined the carrier flow and learned that two neighboring process steps do not automatically create a transport task; a task exists only when the locations are separated and the carrier must move. Third, I separated process completion, load release, request creation, waiting, pickup, delivery, destination acceptance, and the final state update. Finally, I distinguished fleet sizing, dispatching, routing, traffic control, and physical handover instead of calling everything AGV scheduling. This gives me a clearer basis for later modelling and validation.

## Slide 3
THE PROBLEM
Week 03 produced a conditional model—not a confirmed factory scenario.
Sources: Kampker et al. 2023, pp. 2–10; Hall & Sriskandarajah 1996, pp. 510–525; project inference labeled
03
Literature-supported
Cell-finishing routes vary by manufacturer and format.
AGV design contains distinct control decisions.
A real battery-production AGV case exists.
Conditional inference
Physical separation + carrier relocation creates a transport task.
Delays may cause blocking or starvation only under specific buffer and interface conditions.
Still unknown
Cell format and transport unit
Tray continuity and handover
Layout, takt, empty returns, AGV count
Whether AGVs are used at all
Notes: The main problem is now more specific than simply saying that data are missing. The literature supports several parts of the model: cell-finishing routes vary by manufacturer and cell format, AGV systems contain different design and control decisions, and there is at least one real AGV case in rechargeable-battery production. However, the connection to our selected tray-flow case is still conditional. I can infer that physical separation and carrier relocation create a transport task, and that delays may cause blocking or starvation under certain buffer conditions. But the cell format, transport unit, tray continuity, handover interface, layout, takt time, empty-carrier flow, AGV number, and even the use of AGVs are still unknown. Therefore, this is a conceptual model, not a confirmed factory scenario.

## Slide 4
EVIDENCE BOUNDARY
The nearest battery AGV case is real—but not proof of cell-finishing tray transport.
Source: Lee, Park & Jang 2024, WSC, pp. 1–2. Reported site scale; process and material undisclosed.
04
What it proves
Real job records + site configuration
9 AGVs; 100 ports; 4 charging stations
A parking policy was evaluated.
Direct evidence
What it does not show
Material and process are undisclosed.
No formation, aging, EoL, tray, or handover details.
Not disclosed
Implication
Useful for AGV-system methods.
Insufficient to validate our cell-finishing task model or parameters.
Adjacent case
Boundary: case performance cannot transfer to cell finishing without process-specific evidence.
Notes: To test the evidence boundary, I studied the closest public AGV case I found in rechargeable-battery production. The case is valuable because it uses actual job records and a real site configuration with nine AGVs, one hundred ports, and four charging stations, and it evaluates an idle-vehicle parking policy. However, the paper does not disclose what material is transported or which battery process is involved. It does not mention formation, aging, end-of-line testing, trays, or the handover interface. I therefore use it as direct evidence that an AGV-system problem exists in battery production, but only as adjacent evidence for my cell-finishing case. I should not transfer its reported performance results or parameters to my scenario without process-specific evidence.

## Slide 5
NEXT WEEK
Next week tests the literature boundary before any gap or simulation.
Week 04 plan | Nearest-neighbor literature and counterexample audit
05
1. Search nearest neighbors
Target cell finishing + carrier flow + AGV/material handling.
Classify direct, adjacent, and false matches.
2. Audit counterexamples
Build one comparison table.
Test whether process constraints and mobile transport design are already connected.
3. Define evidence needs
Keep only 1–2 candidate gaps.
Turn unresolved interfaces and parameters into expert questions.
Thomas check: Is this concrete enough—and should I prioritize counterexamples or industrial interfaces?
Notes: Next week I will test whether the possible research gap is real before I define a simulation study. First, I will search specifically for research that connects cell finishing, carrier flow, and AGV or material-handling design, and I will classify the results as direct, adjacent, or false matches. Second, I will build one comparison table and actively search for counterexamples that may already connect process constraints with mobile transport decisions. Third, I will keep only one or two candidate gaps and convert the remaining unknown interfaces and parameters into focused expert questions. At this point, I would like to ask whether this level of decomposition is concrete enough, and whether I should prioritize academic counterexamples or industrial interface evidence in the next step.