## Slide 1
TODAY
Week 01 update: from topic orientation to first use-case map
Week 01 group meeting | Robotic systems in battery manufacturing
01
Main message: I am turning a broad robotics topic into a process-aware evaluation framework.
1. What I did
Topic boundary
Battery fundamentals
Process-to-robotics mapping
2. What I found
Robotics value depends on battery process requirements, not only robot capability.
3. What I need
Supervisor decisions on scope, method, and use-case focus.
Notes: Good morning. Today I would like to give a short update about my first week. The main point is that I am turning a broad robotics topic into a more process-aware thesis direction. I will explain what I did, what I found, what questions I have, and what I plan to do next week.

## Slide 2
WORK DONE
This week I produced four concrete starting points.
Week 01 group meeting | Robotic systems in battery manufacturing
02
Output
What I did
Why it matters
Topic boundary
Defined cell manufacturing as the main scope.
Avoids the thesis becoming too broad.
Battery basics
Read Li-ion fundamentals and made notes.
Explains dry room, safety, and quality constraints.
Process map
Mapped electrode, assembly, finishing, and logistics steps.
Creates the structure for robotic application screening.
Use-case shortlist
Selected first candidate robotic applications.
Gives the thesis a possible evaluation direction.
Notes: This week I produced four starting points. First, I clarified the topic boundary. I think the main scope should be battery cell manufacturing. Second, I started reading battery fundamentals. This is important because many robotics challenges come from the battery process itself. Third, I built a first process map. Fourth, I selected first robotic use cases for deeper study.

## Slide 3
THESIS UNDERSTANDING
The focus is application evaluation, not robot controller design.
Week 01 group meeting | Robotic systems in battery manufacturing
03
Included
Battery cell manufacturing
Industrial robots, cobots, AGV/AMR, and vision-guided systems
Technical and economic evaluation
Excluded for now
Detailed robot control algorithms
Detailed electrochemical cell design
Pack assembly and recycling as core topics
Working question
Where can robotic systems create real value in battery cell production, and how can selected use cases be implemented?
Current logic: process requirements -> robotic opportunities -> use-case evaluation -> implementation strategy
Notes: My current understanding is that this thesis is not about designing a robot controller. It is about evaluating where robotic systems can create value in battery cell manufacturing. So I want to first understand process requirements, then identify robotic opportunities, and finally compare selected use cases from technical and economic perspectives.

## Slide 4
BATTERY BASICS
Battery materials explain many robotics constraints.
Week 01 group meeting | Robotic systems in battery manufacturing
04
Battery concept
Manufacturing requirement
Robotics implication
Electrolyte is moisture-sensitive
Dry room and safe filling are needed.
Robots and AMRs must work in dry-room conditions.
Separator and electrodes are thin
Handling must be gentle and accurate.
Vision guidance and special grippers may be needed.
Formation affects lifetime
Cells need controlled charging, aging, and testing.
Tray handling and traceability become important.
Defects affect safety
Inspection and sorting are critical.
Robots can support safe reject flow and quality data.
Notes: Battery fundamentals are important for my topic because they explain the manufacturing constraints. For example, electrolyte is moisture-sensitive, so dry-room operation is important. Separators and electrodes are thin, so handling must be gentle and accurate. Formation affects lifetime, so tray handling and traceability are important. This means robotics must be evaluated together with process, safety, and quality requirements.

## Slide 5
PROCESS MAP
Different stages have different robotic potential and difficulty.
Week 01 group meeting | Robotic systems in battery manufacturing
05
Electrode manufacturing
Mixing, coating, drying, calendering, slitting
Robots mainly support roll handling, sampling, inspection, and logistics.
Medium priority
Cell assembly
Cutting, stacking/winding, welding, filling, sealing
High potential, but difficult because materials are thin and precise.
High but difficult
Cell finishing
Formation, aging, testing, sorting, logistics
Strong near-term potential: sealed cells, trays, repeated handling.
High priority
First conclusion: cell finishing and intralogistics are the most realistic starting points.
Notes: I divided battery cell manufacturing into three stages. In electrode manufacturing, robots mainly support surrounding tasks such as roll handling, sampling, inspection, and logistics. In cell assembly, robotics potential is high, but the difficulty is also high because materials are thin and precision is critical. In cell finishing, cells are already sealed and often tray-based, so I think this is a strong near-term direction.

## Slide 6
CANDIDATE USE CASES
I currently recommend three main directions for deeper study.
Week 01 group meeting | Robotic systems in battery manufacturing
06
Rank
Use case
Why it is promising
Main risk / question
1
AMR / AGV intralogistics
Supports material flow, reduces manual transport, links to traceability.
Dry-room compatibility and MES integration.
2
Formation / testing tray handling
Cells are sealed, tray-based, repetitive, and suitable for economic evaluation.
Interface with test equipment and safety logic.
3
Vision-guided inspection + loading
Connects robotics with quality control and production data.
Need good industrial examples and clear scope.
Optional technical-depth case: vision-guided stacking or housing insertion, but this may be too difficult for the main evaluation.
Notes: Based on the first mapping, I recommend three directions for deeper study. The first is AMR or AGV intralogistics. The second is formation and testing tray handling. The third is vision-guided inspection and robot loading. I may also mention vision-guided stacking or housing insertion as a technically difficult case, but I am not sure if it should be one of the main cases.

## Slide 7
QUESTIONS
I need supervisor input before narrowing the thesis.
Week 01 group meeting | Robotic systems in battery manufacturing
07
Scope
Should I focus on one cell format?
Should module and pack examples only be future trends?
How much battery chemistry depth is expected?
Method
Is a literature-based evaluation enough?
Should I include expert interviews or case studies?
How detailed should the economic evaluation be?
Use cases
Which use cases are most relevant to PEM / eLab?
Should formation/testing be the primary case?
Should one difficult assembly case be included?
Notes: Before narrowing the thesis, I would like to clarify several points. For scope, should I focus on one cell format or compare several formats? For method, is a literature-based evaluation enough, or should I include expert interviews or case studies? For use cases, which ones are most relevant to PEM or eLab?

## Slide 8
NEXT WEEK
The next step is to move from mapping to evaluation.
Week 01 group meeting | Robotic systems in battery manufacturing
08
1. Strengthen literature
Read battery fundamentals and process-focused manufacturing papers.
Complete key glossary terms.
2. Narrow use cases
Select two or three main use cases based on supervisor feedback.
Define their process boundaries.
3. Build scoring model
Evaluate feasibility, quality impact, economic potential, scalability, safety, and traceability.
Expected output: a use-case shortlist and the first evaluation table.
Notes: For next week, I plan to do three things. First, I will read more battery fundamentals and manufacturing process literature. Second, I will narrow the use cases based on your feedback. Third, I will build a first scoring model. The expected output is a clear use-case shortlist and a first evaluation table.